Tea rolling machine

Operate literature

Foreword:

In order you can use the machine safely, and produce high quality tea, please notice the following:

1. This type of machine has two kind motive powder, 380V and 220V, so when selecting and purchasing, the user should consider the supply voltage, when install the machine, you should examine if the supply voltage is suitable for the motor of the machine.

2. For your safety, please install an earthing wire on the outer covering of the machine, the earthing wire could connect with any thread connected point of the machine seat, and make sure it connect well.

3. The electric heating type product uses the 220V electric heating pipe, therefore the supply voltage should be 380V and four wires, and it must have the neutral wire.

- Function and characteristic

The 6CR series miniature tea twisting machine is suitable for the famous and superior tea. It use small barrel, rolling lightly and twisting quickly, this conforms to characteristic of the famous and superior tea leaf’s tender and easy to shape. This machine has many merits: the twisting time is short, the stripping tea rate is high, the broken tea rate is low, and the outer tea strip is tight and evenly.

- Major technique parameter

| Project | Unit | 6CR-15 | 6CR-25 | 6CR-30 |
| --- | --- | --- | --- | --- |
| Twisting barrel | Outside diameter height | mm | Φ150*130 | Φ250*180 | Φ300*210 |
|  | Capacity of the barrel | Kg/ barrel | 0.75 | 3.00 | 5.00 |
|  | Circling speed | r/min | 50±2 | 39±1 |
| Twisting Disc | Inside diameter | mm | 300 | 450 | 560 |
|  | concavity | ° | 6 |
|  | Quantity of edge bone | foot | Outer 9 Inner 4 | Outer 10 Inner 4 |
| Distance of the crank | mm | 65 | 95 | 125 |
| type of supercharge device |  | lever–weight | single–column screw |
| Motor | Kw/V | 0.25/220 | 0.37/380 (220) | 0.55/380 (220) |
| Size(length*width*height) | mm | 500*450*400 | 670*570*600 | 1065*860*706 |
| Weight | kg | 55 | 75 | 100 |

- Operation

1. Preparatory work before operation

- This machine should the lay on the work table steadily, clear out the sundry and dirt on the machine, and please pay attention: there are no any sundry things on the rolling disc and barrel. The operator should send a message before starting the machine, and leave the frame, in case injures the operator.

- Please inspect if the supply voltage according with the motor’s voltage, connect the earthing wire and Protector against Leak Electricity, safeguards the operator and the machine.

- Inspect whether the fastener fitting is reliable, especially whether the screw on the crank loose or fall off.

- There should pour enough lubricating oil into the worm gear reducer, the oil reaching the worm gear middle line surface will be better.

- Turn on the electric power source, make the machine to work 10 minutes with nothing, if it appear the stopping and collision, please shut down the machine immediately and check it.

2. Operation

(1) Carry the twisting lid; make it leave the twisting barrel, then throw in the leaf. When throwing the leaf, it should conform to the standard, it’s suitable for throwing freely, don’t extrude the processing leaf with hand.

(2) After throwing in the leaf, put the lid into the barrel, it is suitable to put in 10mm, and then start the machine to twist.

(3) It should work following the pressurize extent and time requirement of the superior and famous tea’s twisting craft.

(4) Discharging of twisting leaves: after turn down the machine, take out the leaves with hands from the twisting barrel.

3. Maintenance

(1) in the work process, if it appear the collision, stopping or unusual sound, it should be turned off at once, inspect the reason of the malfunction, and get rid of it, then it can work continue.

(2) After ending the work, it should be clear the remaining things on and in the twisting disc, and clean it with cloth. In this processing, it should use water, don’t use fat, because the tea juice only dissolves in water.

(3) After ending the work, it should inspect if the lubricating oil in the worm gear reducer is sufficient, if not, fill in time, and inspect whether the fastener fitting has loosed.

(4) Refuels the points regularly, the fat which uses must be clean, the column and supercharge column should under the proper lubrication condition, the fat can’t be excessively much, in order to avoid it polluting the tea.

(5) When the machine is working, forbid to refuel. When discovering the abnormal impacting, the unusual sound, and so on, it should turn down the machine immediately, find out the malfunction, and get rid of it in time.

- Common machine malfunction and elimination method

| Art no | Common malfunction | Reason | Elimination method |
| --- | --- | --- | --- |
| 1 | Twisting barrel circle anticlockwise or stop | a mistake in connecting the wire with the three-phase motor; the screw on the main crank and main axletree fall off or loose; single-phase motor’s electric capacitor damage | exchange the connected place of the two-phase wire; inspect and screw the screw; change a suitable electric capacitor |
| 2 | The noise of the machine is large | the lubricating oil in the worm gear reducer is not enough, or the worm gear is attrition | Add the lubricating oil, or change a new worm gear |
| 3 | Twisting lid rock too much to hit the barrel | the screw on the bottom of the vertical column loose; the screw linked on the twisting lid loose | Screw the loosed screw |

- Vulnerable fittings

| Production | Fitting | Model |
| --- | --- | --- |
| Rolling machine (6CRW-15) （6CRW-25） （6CRW-30) | Scale | 6CRW-15 |
|  | Scale | 6CRW-25 |
|  | Rolling cylinder | 6CRW-15 |
|  | Rolling cylinder | 6CRW-25 |
|  | Rolling cylinder | 6CRW-30 |
|  | Rolling plate | 6CRW-15 |
|  | Rolling plate | 6CRW-25 |
|  | Rolling plate | 6CRW-30 |
|  | v-belt | 0 type 800 |
| gear box | Worm gear | M2 |
|  | Worm gear | M3 |
|  | Worm | M2 |
|  | Worm | M3 |
|  | Worm gear box | M2 |
|  | Worm gear box | M3 |
| Rolling axletree | Axletree | 205 |
|  | Axletree | 204 |
|  | Axletree | 203 |
|  | Axletree | 202 |