6CJW—40/50 Deblocking Tea Machinery

The instructions

Preface

Thanks for you to select yiyuan brand products, in order to better use this product, produce more top tea, please be sure to read the instruction, in order to avoid the mistakes. Especially the following need pay more attention to:

- These factory products distribute motivation to three-phase and single phase (380 V and 220 V), the user in the points when choose and buy. According to using places shall be determined, and before install should check the electric source is consistent with the product motor.

- For your safety, please be sure to be in machine shell in again on ground, ground wire can fixed in any machine, a bolt (was) connection place, contact must be good.

- Our electric-type (commonly known as burning electric) products using 220V electric heaters, power should be three-phase four-wire system, must be zero wire.

- Use and characteristics

This machine is one of the excellent tea set machines. Through this machine will deblock the group tea caused by rotating, so that to do the next process drying or forming.

The structure of machine is compact, not easy the creation fault, convenient for use.

- The main technical parameters

| Project | Unit | 6CJW—40 | 6CJW—50 |
| --- | --- | --- | --- |
| Structure |  | Mouse cage rotor |
| Deblocking wheel (Diameter*Length) | mm | Ф170×354 | Ф240×526 |
| Deblocking wheel speed | r/min | 850 | 754 |
| Output per machine-hour | kg/h | 140-150 | 400-500 |
| motor | Power | KW | 0.35 | 0.75 |
|  | Speed | r/min | 1400 |
|  | Power source | V | 380V or 220V |
| Size (length * width * height) | mm | 660×460×900 | 830×830×1580 |

- The structure and working principle

This machine is composed of machine frame, motor, driving belt, deblocking wheel, into Ye Dou, the protective cover.

The rolling tea will be put into the deblocking machine, through the fast rotation cage type deblocking wheel to quickly deblock the bulk tea, and the output from machine. That is the complete deblocking process.

- Installation and Test run

- The machine must be installed the anchor bolts, asks to install field leveling, this machine is four legs uniform and ground surface contact, the airframe not be swing.

- Check the connect parts without loose screw.

- Put the grease onto the bearing.

- To properly connect the rack with the earth line, in order to prevent the electric shock.

- The motor is connected to the power supply. The power supply circuit shall be equipped with switches and electrical protection device, such as a fuse, electric shock protector.

- The machine will be rotated by using the chain belt, and also will be checked for whether the block and other abnormal situations.

- All the conditions are normal, and then can be opening and idling. Stable operation without exception, can be put into production use.

朗读

显示对应的拉丁字符的拼音

为翻译结果评分

- The use and operation

- Firstly open and test run, and then gradually into the tea group, do not put too much at one time.

- Stop the machine after the tea out, and clean.

- Maintenance

- In order to ensure the normal operation, and prolongs the service life of the machine, must regular maintenance the machine.

- When the machine is in working process, found to have abnormal impact and noise, should immediately stop and check, after troubleshooting then can be work.

- Regularly to gas the bearing.

- To adjust appropriately the tightness of the leather belt, too loose and too tight are all not good.

- Every year after the end of the machine work, should clean, inspect for damage, repair after storage.