6CMD-40/7 troughs multipurpose machinery

The instructions

Preface

Thanks for you to select yiyuan brand products, in order to better use this product, produce more top tea, please be sure to read the instruction, in order to avoid the mistakes. Especially the following need pay more attention to:

- This factory product distribution motivation have three-phase and single phase (380 V and 220 V), the user in the points when the choose and buy.According to using places shall be determined, and  before install should check the electric source is consistent with the product motor.

- For your safety, please be sure to be in machine shell in again on ground, ground wire can fixed in any machine,a bolt (was) connection place, contact must be good.

- Our electric-type (commonly known as burning electric) products using 220V electric heaters, power should be three-phase four-wire system, must be zero wire. For convenience, the top hole of plug is used as a zero wiring terminal.

- The wood coal ( coal or wood ) products all to be using closed furnace and flue, chimney height was to be careful researched and determined. do not arbitrarily truncate the chimneys by random brought, also do not match with another extension, so as to avoid bad burning or the heat escaping too much to influence the tea quality.

- Gas type tea machine is suitable for liquefied petroleum gas. If use pipe gas or natural gas, gas stove should be changed accordingly, and gas stove should be according to the directions corresponding to the selected valve, and use resistance to high pressure, high temperature, acid and alkali resistant pipe to be connected with the air inlet interface. Check the intake hose is damaged or not, such as broken, should be immediately replaced in order to ensure safety.

- Use and characteristics

This product is applicable to the famous high-grade bar tea carding, plastic operation. The tea product has advantage of  tight straight, shoots, seedlings show, jade green color.

- Technical parameter

| Project | Unit | 6CLZ-60 Electric, firewood, gas |
| --- | --- | --- |
| Many troughs boiler | Boiler weight | mm | 400 |
|  | Trough quantity |  | 7 |
|  | Length | mm | 817 |
|  | Times of to-and-fro | Times/min | 120-175 |
| Operation quantity | Kg/h | 7 |
| Heating energy consumption | Eledtric heating | Kw/h | 12 |
|  | Burning heating | Kg/h (firewood) | 10 |
|  | Gas heating | Kg/h | 0.6 |
| Motor | Kw/v | 0.55/380 （220） |
| Appearance size (L x W x H) | Mm | 1270x544x790 |

Note: appearance height of burning fire-wood not included in the chimney.

- The use and operation

  - preparing work

    - Please be sure to check the supply voltage using the products are consist with the choice of electrical voltage, and properly connect with the earth wire and the electric shock protector, in that ensure the safety of people and equipment.

    - Check the fastener is reliable, tighten the loose fasteners.

    - Clean the machine on the surface of the glove.

    - Switched on to start the machine, 0.5 hours of air operations, to check the machine operation is normal, there is blocking, collision and abnormal sound phenomenon or not.

  - operation and use

    - When heating pot and pot temperature rises to start the machine and rotate the speed hand wheel as beginning slow. When sense the pot warm and burning, please use the tea oil to quick wipe the pot. At that time the pot should be smoking, and then use the cloth to wiping the pot surface. Within 4-5 minutes for leaf moisture content to decrease about 20%, then stopped the machine and lift pot handle, so that let the tea rapidly to be discharged outside the cooker.

    - Speed the boiler for one minute, then drop the leaf (per pot leaf weight about 1Kg). The leaf weight of each pot should be even.

    - The use of the machine, please master pot temperature change, prevent the color yellow, dark and high fire taste.

    - For the gas type carding machine, after open the gas valve switch in two seconds, and press the ignition button to ignite the whole burner. When delayed ignition after burner, if not lit (or not fully lit), then close the ball valve switch and ignite again.

  - Maintenance

On the work process, if found in machine clamping resistance, collision and abnormal sound phenomena, should immediately stop and check fault and eliminate it, refuses to operate in ill.

- Common mechanical failures and maintain methods (gas) mainly associated parts:

| Failures Parts | Can’t ignite | Appear yellow fire | Uneven fire | Abnormal sound | Maintain methods |
| --- | --- | --- | --- | --- | --- |
| Gas source | ○ | ○ |  |  | Check the gas, if not gas should replaced the source |
| Burner |  | ○ | ○ | ○ | Clean the burning hole |
| Electrical parts | ○ |  |  |  | Adjust the ignition needle place, if still can’t ignite, should maintain and change. |
| switch part | ○ |  |  |  | Check the foreign matter |
| Spray nozzle | ○ | ○ |  | ○ | Clearing the nozzle blockage |
| Pressure reducing valve | ○ | ○ |  |  | The valve is not ventilated, should be replaced |
| Pipe |  | ○ |  | ○ | Check the tightness |
| Rules of operation | ○ |  |  | ○ | According to the operation procedures |

- Easy damaged part

| Name | Type |
| --- | --- |
| Connecting rod | Single |
| Connecting rod seat | Single |
| Connecting rod pin bushing | Single |
| Sliding sleeve | Single |
| Pin shaft | Single |
| U type electric heating tube | 2.5KW/220V/branch |
| U type electric heating tube | 4.5KW/220V/branch |
| Triangle belt | B1041.A1168 |
| Pot | Cold plate production |
| Firewood stove | Single |