6CR-35/40 type of tea rolled machine

The instructions

Preface

Thanks for you to select yiyuan brand products, in order to you can better use this product, produce more top tea, please be sure to read the instruction, in order to avoid the mistakes. Especially the following need pay more attention to:

- This factory product distribution motivation have three-phase and single phase (380 V and 220 V), the user in the points when the choose and buy.According to using places shall be determined, and power supply conditions Install the check to power and product motor is consistent.

- For your safety, please be sure to be in machine shell in again on ground, ground wire can fixed in any machine,a bolt (was) connection place, contact must be good.

- Our electric-type (commonly known as burning electric) products using 220V electric heaters, power should be three-phase four-wire system, must be zero line.

One, Use and characteristics

1, use

This machine is applicable for the rolling work of the black tea and green tea, and which twist the withered leaves or fixation, to destructe the leaf cells for the dying work.

2, characteristics

(1), Simple structure, reasonable layout.

(2), Excellent tea quality, the cable tight straight, cell to be suitable damaged and few fannings, less running tea.

(3), Stable running, convenient operation, safety and reliable.

(4), Proper edge bone offset angle, a good orientation, no running tea.

(5), Pressurizing device for floating type, cover can rotate, tea ruffled rapidly in the barrel, it is not easy to be crushed, while high efficiency.

Two, The main technical parameters

| Item | Unit | 6CR-35 | 6CR-40 |
| --- | --- | --- | --- |
| Form |  | Single acting |
| Transmission form |  | Stand-alone driving |
| Compression form |  | Single column screw floating pressure |
| Rolling bucket | External diameter*height | mm | 350x250 | 400x300 |
|  | Capcity of tea | Kg/bucket | 10-12 | 12-14 |
|  | Rolling speed | r/min | 38-40 | 48-52 |
| Internal diameter of rolling bucket | mm | 700 | 760 |
| Tea machine | Form |  | Pendulum locking center out of tea |
|  | External diameter | mm | 200 |
| Motor | Model |  | Y90S-4 |
|  | Power | KW | 0.55 | 1.1 |
|  | Rolling speed | r/min |  | 1400 |
|  | Voltage | V | 220 | 380 |
| Crank center distance | mm | 160 | 165 |
| Rolling time | Green tea | Min | 35 | 10-25 |
| Output | Green tea | Kg | 22-35 (fixation) |
| Outlook size | mm | 1100x1000x1020 | 1200x1100x1200 |
| Unit machine weight | kg | 150 | 170 |

Three, The structure and working principle

This type machine is consisting of gear slowdown transmission mechanism, rolling and door of output mechanism, crank swing mechanism, rolling and compression mechanism.

They are main apply for three crank rotating, letting the rolling bucket fixed on the rolling disc do relative to 360° eccentric rotary motion. The tea would be rolling on the bucket pressure and rolling disc work up to finish the rolling work.

Four, The use, repair and maintenance

1. The preparation of starting up the machine

- Examine the motor oil of the gear box. Put the 10# motor oil into the box while oil is shortage.

- Examine the connecting parts of bolts, screws and pins are secured.

- Examine the electrical equipment is reliable, and clearing the sundries of machine. Properly connected to the earth wire.

- Pulling the belt, examine the working condition to confirm the machine would be test to run empty.

2. Operation method

- Stop running, open the pressurizing cover and close the output door, then add enough amount of enzyme-denatured leaf or withering leaf.

- Close the pressurizing cover and make the cover into the bucket about 30mm, then began operation, later pressurizing step by step up to enough. Later decrease the pressure and rolling in one minute, and adopt the tea juice. Then can output the tea, stop the machine and clean it. For ready to began next rolling work.

3. Maintenance

- Must be regularly maintained the machine in order to ensure the normal operation of the machine, and prolong the service time.

- In the working process of the machine, should immediately stop and check when found the abnormal shock and noise. Troubleshooting and work again.

- Note that the heating condition of motor and gear box. The temperature of motor could not exceed 65℃, the temperature of gear box oil could not exceed 80℃, each rolling bearing’s highest temperature could not exceed 70℃.

- Periodically to lubricating each part of needing lubrication. Note the oil condition of gear box.

- Should clean the machine after working every year. Examine the easy damaged part so that to repair and regeneration. Relax the triangle belt, and smear anti-corrosive grease on the easy rusted part.

Five, Machinery installation

The machine has the advantage of simple installation. Put the uninstalled machine in the selected position, and put the tripod on three pouring hole, and put on the foot screws. Then correct the rolling disc level, and pour the cement mortar, after the cement mortar become firm, remove the support, then gradually tighten the screws, also M12 expansion bolt available. Measure the level of the rolling disc to the tightening of the nut so far, then the installation finished.

Six, Easy damaged parts

| Number | Name | Material | Quantity | Note |
| --- | --- | --- | --- | --- |
| 1 | High-speed gear | 45 | 1 |  |
| 2 | Straight gear | 45 | 1 |  |
| 3 | Big bevel gear | 45 | 1 |  |
| 4 | Small bevel gear | 40Cr | 1 |  |
| 5 | Outside goniale | ZL7 | 12 |  |
| 6 | Inside goniale | ZL7 | 5 |  |
| 7 | Screw cap | ZQSn6-6-3 | 1 |  |
| 8 | Screw rod | 45 | 1 |  |