6CZS-300 Steam heat Fixation Machinery

The instructions

Preface

Thanks for you to select yiyuan brand products, in order to better use this product, produce more top tea, please be sure to read the instruction, in order to avoid the mistakes. Especially the following need pay more attention to:

- The products of factory distribute three-phase and single phase (380 V and 220 V), the user in the points when choose and buy. According to using places shall be determined, and power supply conditions install the check to power and product motor is consistent.

- For your safety, please be sure to be in machine shell in again on ground, ground wire can fixed in any machine, a bolt (was) connection place, contact must be good.

- Our electric-type (commonly known as burning electric) products using 220V electric heaters, power should be three-phase four-wire system, must be zero wire. For convenience, the top hole of plug is used as a zero wiring terminal.

- The wood coal (coal or wood) products are all to be using closed furnace and flue, chimney height was to be careful researched and determined. do not arbitrarily truncate the chimneys by random brought, also do not match with another extension, so as to avoid bad burning or the heat escaping too much to influence the tea quality.

- Gas type tea machine is suitable for liquefied petroleum gas. If use pipe gas or natural gas, gas stove should be changed accordingly, and gas stove should be according to the directions corresponding to the selected valve, and use resistance to high pressure, high temperature, acid and alkali resistant pipe to be connected with the air inlet interface. Check the intake hose is damaged or not, such as broken, should be immediately replaced in order to ensure safety.

- Use and characteristics

This machine is composed of a steam fixing chamber, cooling machine, winnowing tea components, steam heat furnace and other parts. It is suitable for green tea fixing operation. The steam fixing chamber uses the steam as the fixing medium and to achieve continuous tea contact. In the steam fixing indoor" hyperthermia steam" destruct the activity of the fresh leaves, and remove the smell of fresh leaves, make its soft shrink, and generates good flavor, keep the green degree. Cooling machine through the air for fixing the tea fast drying, and by the strong cold air cooler rapid cooling, drying, steamed leaves can keep good green degree, and can be directly used for the process after traditional tea process.

- Structure

- the steam chamber

The steam fixing chamber is combined by the inlet pipe, the drum member and an inner shell and other components. Water vapor enter into the inner shell to be formed within a certain pressure steam fixing chamber to maintain a certain temperature, the" high steaming hot steam" -- fixing medium, the fresh leaves are transmitted by the stainless steel mesh belt conveyor even across the steam fixing chamber. Mesh belt speed control by speed regulating motor, depending on the quality of fresh leaves and water content of effective regulation of belt speed, so as to achieve good fixing effect.

- cooling machine

Cooling machine comprises transmission part, air coolers, winnowing tea components, air bag and other components. fresh leaves are transmitted by the stainless steel mesh belt conveyor, the air bag by hot-air drying, tea leaves are turned for changed tea heated direction in the transportation process, through high, middle, low three different temperature zones, to achieve uniform, rapid dehydration, drying, and the dried by air cooler, and then the fixing leave quickly cooling, finally by winnowing component send. The stainless steel mesh belt slip regulate the motor driving speed, can control a large range of net belt speed, so as to effectively control the drying and cooling effect of tea.

- Main technical parameter

| Project | Unit | Parameter |
| --- | --- | --- |
| Output per machine-hour | kg/h | 220-320 |
| Fixing time | min |  |
| Steaming temperature | ℃ | 100-150 |
| Dehydration time | minute |  |
| Hot blast rate | m3/h |  |
| Hot-blast temperature | ℃ | 120-150 |
| Steam chamber | Belt width | Belt speed |
|  | 800（mm） | 1.3～13m/min |
| Cooling machine | Belt width | Belt speed |
|  | 800（mm） | 0.94～9.43（m/min） |
| Air cooling speed | r/min | 1170/752 (two grade) |
| Cooling fan |  |  |
| Winnowing fan |  |  |
| Well spreading leaves motor |  |  |
| Appearance size (L*W*H) | Steam chamber | Cooling machine |
|  | 2920×810×1600 (without exhaust pipe) (mm) | 4700×1360×1960（mm） |

- Main operating principle

Steaming fresh leaves are put into the hopper, through the spreading equipment to be even sent into the steaming chamber. the tea into the steam fixing chamber, enzyme activity is destroyed, so that fresh leaf soft reduction, and promote appropriate chemical changes, and remove the smell of fresh leaves to finish the steaming operation, then to be moved by the mesh belt into the cooling machine. The hot air bag in front of cooling machine blow hot air by to heat and dry the moisture content of the steaming leaves. Through the middle and posterior part of the temperature decreased gradually, and the cold air machine high strength fast cooling and winnowing component cooling again to achieve that rapidly drying and cooling functions, to make the incompletely destroyed enzyme cannot play micro fermentation and maintain the fixing leaves green, and satisfies the kneading and other traditional post process.

- Installation and adjustment

- The machine lifting (chimney is not installed) is divided into five parts: the fixing section, the dewatering section, the steam generator, the winnowing machine, and the others (such as pipe, chimney, etc.).

- The installation should be at the smooth concrete ground.

- The chimney and a smoke outlet position and operator position should be forethought and arrange for the chimney smoke outlet to the outside. Then using three wires to equal tension at the top part and fixed firmly in the dowel pin, lest the wind will blow down the chimney. The steam heat generator preferably installed in separate rooms, in order to keep the tea plant health.

- The main engine was in place, and to adjust the height and level to join with the steam generator tube, so that the each foot are all contacted with the ground, and the let the frame keep level.

- Check the screw are fastening, oil is sufficient, with net location is correct, and wrapped the steam and air input pipe with asbestos board ( 20) and tin platinum paper, reduce heat loss.

- Users should connect the fuse and leakage protection switch in the charging line, and make the machine casing and electrical box, all fans to connected with the earth line for the safety, the machine power is four phase three wire 380V.

- Connect the power to inspect the motor turning right or not.

- Connect the water source, the water should be consistent with the boiler soft water standard, so lest the water boiler scaling.

- Through the installation and checking to confirm that the installation is correct, and then can be running. Empty running time is not less than 30 minutes, running stability, and no abnormal noise.

- Use and operation

- Burn the stove

Fire stove: before fire the stove, open the valve, the machine can automatically maintain the water level of the pot. Observe the water level and ball cock condition through the transparent window. The ball cock should keep running water in the firing furnace, and then can fire the furnace, dry burning will burn water pot. Open the ash door, first fire the wood, open the fan, when a part of burning charcoal the user can add coal to the furnace center, and gradually spread to the edge. When coal burned 5-7 minutes to open main fan and off the ash door, open the throttle to let air into the furnace below, gradually increase to make the normal combustion, neither lack of air do not too much air. Moreover open widely the throttle to produce a tapered fire curtain on the coal. After few minutes burning, then can regulate again to approach the stable state.

Coaling way: the coal must be added to the middle part of the grate, and compact it. When firepower is poor, the user can hook the coal at the outer circle, and then put the new coal into the middle part, and compact them. Then forming the intermediate high surrounded by low steamed bread shape, the surrounding coal will not block the bocca. If burnt cinders can not fall from grate seam, must dig the burnt cinders from the furnace door, to ensure that the new coal can be added and not block the crater. Close the stove door after digging or adding.

When add coal or dredge the furnace, should not dredge the refractory clay, refractory brick, so as to avoid damage.

Quenching furnace: first close the combustion-supporting fan and fire curtain, after the temperature reduced, then withdrawal the burnt coal, last open the ash door to dredge the slag and close the ash door. When open the combustion-supporting, user can not open the ash door.

Note: when the ventilator starts 5 to 7 minutes must start the main fan, it does not burn the hearth and affect the service life. After quenching furnace, the main fan must continue to be open. The air temperature dropped to below 60℃ and then shut off the main fan.

When a special case of the main air blower stops rotating, it must be closed combustion door and fire curtain door, then dig the burnt coal and shutting down draught fan, close the draught fan as soon as possible, decrease the temperature of the hearth, lest affect the using life.

- Tea fixation翻译结果重试

抱歉，系统响应超时，请稍后再试

- 支持中文、英文免费在线翻译

- 支持网页翻译，在输入框输入网页地址即可

- 提供一键清空、复制功能、支持双语对照查看，使您体验更加流畅

As varieties tea, old and young, and different water content, thus realize to" according tea to make tea, watching the days to make tea", could not do one way for any tea.

The fixation: General furnace temperature need to burn high, when the steam thermometer indicates the temperature is higher than 100℃, then can start to fixing, low temperature requirements of fixation time is long, high temperature the steaming time is short, in the condition of fixing well, the short time is better. Steaming time can be adjust stepless in 20 seconds to 60 seconds, and adjust the network speed, regulate the knob of the tachometer in the electric appliance box.

The dehydration: dehydration time is confirmed by tea moisture content, the shorter the better, the color is green. To achieve the drying degree requirements need as soon as possible, when regulating the speed, user should adjust the knob of the tachometer, so that to achieve the desired speed.

- Adjust the tea quantity

Fresh leaves putting into the hopper can be automatically putting up. Even impeller makes fresh leaves to maintain a certain thickness, and the impeller can be adjusted up and down, fresh leaf layer thickness should be less than 30 mm, easy to fixing can be thicker.

- Control of electric cabinet

When using, firstly open the power switch, after the power is switched on, power indicator lighting indicates the power supply is switched on.

Fixing section, with starting belt to press the green button and open the switch below the table right, and then gradually adjusting knob pointer gradually increased to reach a tachometer required speed. At fixing should open the cooling fan switch, the end of all work should off the switch to the initial position, then cut off the power switch.

Dehydration, also open the power switch, power indicator lighting is showed that the power is switched on. First open the net belt press belt motor button, then open the governor switch speed, reach the required speed, when shutting down should decrease the speed to 0 then to off all switches. When using the turning impeller, should open the motor switch.

- Maintenance

- Before ignition, should open the fan up-down wind board to running for 5 minutes to blow the flue dust.

- Check the furnace lining is intact, if find off should repair it in time, lest it burns the furnace.

- Observation the ash condition of hearth and smoke pipe, if more ash, should remove smoke tube and clean it.

- In the use of the process, pay attention to the heating of the motor. The motor temperature shall not exceed the allowable temperature of motor bearing and gear box, and gear box temperature shall not exceed the allowable temperature.

- Frequently check the movement of friction and the gear box lubricating oil are calibrated altitude.

- To avoid fouling the water pot, please use the boiler water softener, water dries burning is forbidden.

- It is strictly prohibited to blocking the steam output pipe or modifying small.

- Frequently check each part of net belt running condition, if the net belts take partial, stop running and out of the chain, should adjust in time.

- Frequently check the fan, motor running condition and temperature rising condition when the machine is in operation. The motor and bearing temperature rising can not exceed more than 75℃, cooling machine main motor running 160 hours need replace new oil, and clean the internal oil. Every half year shall be replaced oil again, and in the work should be regular add lubricating oil, lubricating grease in grades 40 to 50 # speed reducer lubricating grease.

- Regularly check the transmission parts, wearing parts condition. Should be timely repair or replace.

- Steam heating machine parts should be maintenance in each tea period, to be repaired each year.