Multi-purpose loose bag screening powder machine

（JY-6CWM-80）

Product specifications

Respect of customer:

Thanks for you to select our company produced the "yiyuan" tea machinery equipment, our products will be your good helper.

"yiyuan" tea machinery equipment, with Taiwan modern tea machine advanced manufacturing technology, novel design, advanced technology, reliable performance, the applicable widely; the tea by the process of "yiyuan" machine, tea the bands tight knot, aroma is pure, shang bright, taste mellow, the aftertaste is long; Greatly improve the product quality and value, is the first choice of tea in initialhandling and deep processing.

The company wholeheartedly provided the new and old customers with all kinds of standalone or complete sets of equipment, provide tea factory process design, equipment selection, installation, debugging and supporting equipment tea technology consulting, guidance, and provide the high quality post-sale service. Welcome to negotiate business.

To make you can correct operation and use of equipment, we choose for you write the "product operation instruction", and sincere hope you:

Be sure to read in detaile before use!

Sincerely welcome you to put forward valuable comments and suggestions about our products and services.

Thanks

CONTENTS

One, Safety Caution	3

Two, Product use, features and main component parts	4

Three, the main technological parameters	4

Four, control circuit principle diagram	5

Five, installation and debugging	5

Six, use and operation method	6

Seven, common fault and elimination method	6

Eight, Maintenance	7

Nine, transportation and storage	7

Appendix I: accessories list	7

Contact Us	8

# One, Safety Caution

1, this machine can only by the person who is familiar with machine performance, and related safety operation knowledge to operating, preserve and maintenance.

2, strictly according to operating rules to operate and use this machine.

3, the machine must have a good grounding to ensure safety, according to the mark of the ground to grounding connection,

grounding lead wire should be nominal section area of the soft copper wire was 2.5mm2 above, and the leakage protection devices.

4, operation can't wear hypertrophy loose clothes, working clothes to tight, and fasten the buttons, do not wear slippers, the long hair to dish up, and a good working cap, lest baggy clothes or hair is involved in transmission components, cause accidents.

5, the machine running, the operator is prohibited to far away from the machine, others close to the machine.

6, the machine when not in long-term use should be cut off the power.

7, for the machine without authorization, is prohibited to disassemble and the restructuring, if  every user without authorization to remove, restructuring then lead to the function is reduced, and the damage to equipment or cause safety accidents, and our company is not responsible for.

8, in order to use the equipment, avoid  personal injury accident, please be sure to understand equipment related parts all kinds of security paste logo:

A, safety logo:

B、paste position:

Safety identification vague or loss , shall buy to our company, then stick it again!

# Two, Product use, features and main component parts

1, product use

The machine used to package the tea ball after rubbing loosen, so that the tea was loose state, and the foam generated in the process of tea leaves removed from the system, is the main tea processing equipment.

2, the product features

# The cylinder machine with all the materials used galvanized sheet or stainless steel,not easy to rust; within barrel increase, lengthening, with a belt variable speed transmission parts, universal joint bearings, noise reduction,not easy to damage; played with a compact structure, design reasonable, safe and efficient, the use of light and so on.

3, main composition parts

# Loose bag screening powder machine consist of frame, roller, outer garment, motor,control switch and other main components, combination by scientific and strict assembly process.

Three, the main technological parameters

| Number | Item | Unit | Parameters |
| --- | --- | --- | --- |
| 1 | Shape dimension (long x wide x high) | mm | 1375×980×1460 |
| 2 | Tank diameter | mm | 780 |
| 3 | Roller internal length | mm | 750 |
| 4 | Roller rotary motor | power | KW | 0.37 |
|  |  | Rotate speed | r/min | 1400 |
|  |  | Rated voltage | V | 380 |
| 5 | Roller speed | r/min | 36 |
| 6 | sieve diameter | mm | 6 |

Four, control circuit principle diagram

# Five, installation and debugging

1, this machine should be installed  on the flat ground, and the wheel fixed will make the machine to get stuck in the ground .

2, power test run for 10 minutes or more, no abnormal noise during operation, no abnormal vibration, and no other common failures occurred.

3, the drum balance should be adjusted, so that the inner drum in a horizontal position.

4, combined with the switches and the control box of the function buttons, the functions for debugging, everything is normal before put into use.

Six, use and operation method

1. The wires plug access to general supply.

2, put away tea utensils at the mouth of the tea, put the tea ball into the loose charter flights, one time for tea ball to put around 8kg.

3, press the start switch, so that the inner cylinder rotation, the tea ball by throwing drum roll and turn to loose.

4, loose end, just by tilting the joystick to exit rollers, can be automatically out of tea.

5, turn off the power, clean Grottoes, and clean workplace.

Seven, common fault and elimination method

Equipment in the operation process, if discovery is unusual should immediately stop to check and remove the faults rear can be reused.

Common fault and elimination method see the table below:

| Fault phenomena | Fault reason | Elimination method |
| --- | --- | --- |
| Automatic stop | Blown fuse / external power supply is not imported | Replace the fuse / right external supply |
| Abnormal sound when running and excessive vibration | Collision friction / pulley, wheel motor screw loose / other parts of the screw loose | Remove obstructions / fastening screws |
| Speed can not reach ratings | Voltage is too low/instrument aging | Back to normal voltage/replace instrument |
| Drum don't have the power | Three-phase electricity lack phase/belt too loose/carbon brush wear | Connected to the line / adjust the belt tension degree / replacement carbon |
| The body charged | Inductive voltage/wire damaged/motor burn out | With the cross-sectional area more than 2.5 mm soft copper wire to groud, replace or repair damaged wire/replacement motor |

# Eight, Maintenance

1, often check every fastening parts screw loose phenomenon, if have become loose, timely reinforcement.

2, often check transmission belt wear and degree of tightness, don't apply to use, should be replaced or adjust the tensioning device. The machine work, each day should be filled with oil in rotatingbearings and bearing rings and each of the active portion of a period of time to use should be obliterated oil.

3, regular charging all lubricating points lubrication oil.

4, keep the triangle leather belt clean, don't dye grease, in case of sliding, such as triangle leather belt slack, need to loosen bolts relaxation mobile adjustment frame.

5, tea season ends, cleaning machines, filling cleaning oil, replacement of damaged or have excessive wear of parts.

6, the machine unused for a long time, and store in dry, ventilated place,prevent  rain, moisture and pollution. Commissioning and start a regular basis to check the machine performance is normal or not.

# Nine, transportation and storage

1, The machines in transportation and storage process, not collision, damp,under pressure.

2, The machines banned mixing with corrosive or toxic substances .

3, The machines should be stored in a ventilated, dry in the warehouse.

# Appendix I: accessories list

| Name | Quantity | Note |
| --- | --- | --- |
| Shock absorber | 1 |  |
| Product specifications | 1 |  |

Note:

The Company reserves the right to change product design, subject to change without notice. If the products listed in the figure does not match with the physical, to product-based.

# Contact Us

Beijing Yiyuan Economic Trade Ltd

Tel: 8610-8869-1269

8610-5269-0547

Fax: 8610-6868-3582

8610-5269-0549

Tea web: http://www.teanet.com.cn

English Web: http://english.teanet.com.cn

Tea E-mail: sales@teanet.com.cn

Machine Web: http://www.mycotrade.com/enm.htm

Machine E-mail: sales@mycotrade.com

Agri web: http://www.seednet.com.cn

Agri Email: sales@seednet.com.cn

Tour web: http://www.ailitrip.com

Tour Email: aili@ailitrip.com