Do green humidity control equipment

（JY-6CZK-20）

Product specifications

Respect of customer:

Thanks for you to select our company produced the "yiyuan" tea machinery equipment, our products will be your good helper.

"yiyuan" tea machinery equipment, with Taiwan modern tea machine advanced manufacturing technology, novel design, advanced technology, reliable performance, the applicable widely; the tea by the process of "yiyuan" machine, tea the bands tight knot, aroma is pure, shang bright, taste mellow, the aftertaste is long; Greatly improve the product quality and value, is the first choice of tea in initialhandling and deep processing.

The company wholeheartedly provided the new and old customers with all kinds of standalone or complete sets of equipment, provide tea factory process design, equipment selection, installation, debugging and supporting equipment tea technology consulting, guidance, and provide the high quality post-sale service. Welcome to negotiate business.

To make you can correct operation and use of equipment, we choose for you write the "product operation instruction", and sincere hope you:

Be sure to read in detaile before use!

Sincerely welcome you to put forward valuable comments and suggestions about our products and services.

Thanks

CONTENTS

One, Safety Caution	3

Second, The product characteristics	5

Three, operating rules	6

Four, maintenance	7

Five, the common fault and elimination method	8

Six, main technical parameters	8

Seven, accessories list	9

Contact Us	10

# One, Safety Caution

1, dehumidifiers application-specific power supply line, power line cross-sectional area greater than 1.5mm2, plug-and-socket reliable.

2, with three-hole power outlet socket must have a reliable ground, and connected to the receptacle ground pin.

3, Do not move or collection will be the machine on its side or upside down, otherwise it will cause compressor failure.

4, use, keep the air inlet and outlet flow from the wall at least 50 cm.
5, Do not stick thin, hard object into the body, in order to avoid failure or risk. 
6, do not use any relay, extension cords or adapters to connect the machine, or plastic may melt, or even fire.

7, the unit should not be placed on the stove, heater and other heating equipment will be next, or plastic may melt, or even fire. 
8, Do not be subject to direct sunlight or wind and rain places dehumidifier, this machine is for indoor use.

9, a problem occurs (such as sending burning smell, etc.), immediately turn off and unplug the machine, it may cause fire, resulting in new problems.

10, Do not place vulnerable to the effects of chemicals used dehumidifier, into the atmosphere of drugs or solvents will adversely affect the machine.

11, need a long time, unplug the power cord.

12, cleaning the machine, first shut down and unplug the power cord, otherwise easily lead to injury.

13, continuous drainage, please put away the pipes for drainage flow. If the temperature around the pipes may freeze, will not be allowed continuous drainage.

14, Do not repair, disassemble or modify the machine, otherwise it will cause a fire or electric shock.

15, Place the unit securely placed on the premises, if the machine overturned, will the water tank leakage, damage to surrounding objects, and thus cause a fire due to leakage or electric shock.

16, please wipe the dust on the power cord, then plugged in firmly. If the plug is not plugged in, the dust may accumulate, resulting in fire or electric shock.

17, do not come into contact with water may use the premises dehumidifier. The opportunity to water may leak and cause fire or electric shock.

18, Do not plug the power cord of the way to switch the machine, otherwise it will cause a fire or electric shock.

19, Do not damage or modify the power cord. If the power cord is damaged, in order to avoid danger, must be authorized by the Company or the replacement service provider.

In order to use the equipment safety, avoid personal injury accident, please be sure to understand equipment related parts all kinds of security paste logo:

A, safety logo:

B、paste position:

Safety identification vague or loss , shall buy to our company,

then stick it again!

Remind the user:

① microcomputer control dehumidifier, humidity sensor is a precision instrument, there is a strong corrosive gas and dust environment will lead to major equipment failure.

② The machine does not have explosion-proof function, the

flammable, explosive gases, dust, chemicals, biological products and other special requirements of the environment is strictly prohibited.

③ If the above environments, resulting in machine damage, not covered by the warranty.

# Second, The product characteristics

1, the shape of the structure introduced

2, the control panel instructions

# Three, operating rules

This machine makes the blue  humidity control equipment, in 10% -99% relative humidity at any point between the setup and control.

1, steps

① Insert the plug into the correct power supply, the digital display window shows the current humidity, and have [rushing] two sound the machine into standby mode;

② the rise and decline of key by pressing the button control of the  needed temperature;

③ Press the on / off key, run lights, the machine is running;

④ Press the on / off again, running lights off, shut down the machine into standby mode.

2, timer switch

① When the machine is in standby mode, press the timer button, digital display flashing, this time can be increased by pressing the up key and the down key setting 1-24 hours after the scheduled start time, timing lights;

② When the machine is turned on, press the timer button, the digital window flashing, this time can be increased by pressing the up key and the down key setting 1-24 hours after the scheduled shutdown time, timing lights.

Note:

1, as the machine's electrical control touch switch, so do not try to hit any key.

2, the machine off, wait 3 minutes to boot again.

3, using computer control, when the humidity reaches the set value, the compressor and fans will automatically stop working.

4, the machine has power failure memory function when power is restored after power failure, the machine can be set according to the original state of operation. In case of power outages, please be sure the staff before leaving the power plug pulled out.

5, stop use, unplug the power.

# Four, maintenance

● Computer control and protection functions

1, automatic defrost protection functions

Defrosting, the compressor stops running, the fan is running.

2, the compressor start delay protection functions

Compressor stops, the automatic delay 3 minutes before starting again.

3, machine malfunction indication function

When the temperature sensor error, the display window will display E1 an error code 1s with the current humidity 30s alternating shows.

When the humidity sensor error, the display window will display E2 the error code 1s and display window 50 display  30s  alternately shows that maintenance personnel can quickly according to the fault code troubleshooting.

● Maintenance

Cut off the power before maintenance, and disconnect the plug from the power outlet.

1, cleaning air filters

Air filter net attached to too much dust, air flow will decrease dehumidification capacity will be reduced, must be cleaned regularly, at least fortnightly inspections. Such as the environment have more dust, it must be cleaned once weekly or even daily. Cleaning, unscrew the front panel before the Ministry of screws, remove the front panel. Tap filter or vacuum cleaner to remove dust on the filter, or filter placed in warm water (≤ 40 ℃ and add a small amount of neutral detergent) in the wash and rinse with water then drying.

Note:

a: filter net is not direct sun, or roasted, in order to avoid distortion.

b: dehumidifier should be installed a filter net before starting.

2, the body clean

(1) Use soft dry cloth and wipe clean;

(2) If the body covered with dust or dirty, please wipe with a mild detergent, then dry cloth dampened with water will be cleaner wipe. Prohibited use of solvents, polishing powder cleaning the body, so as not to damage the surface.

(3) No water rinse, so as to avoid leakage caused by poor insulation.

# Five, the common fault and elimination method

General troubleshooting

| Fault phenomena | Cause analysis | Elimination method |
| --- | --- | --- |
| The machine can not operate | Power failure; power switch is not turned on; the power plug is not plugged into an outlet;fuse burnout | Restoration of power supply; power is restored; to plug in the socket; replace fuse |
| The machine dehumidification result is bad | Fouling the air filter net; dehumidifier out of the wind; obstructions; doors and windows open; refrigerant leaks | Clean the filter net; to remove obstacles; close doors and windows and use curtains shade; and vendor repair |
| Leak water | Tilt the machine outlet pipe plug | adjust the level panel of the machine to remove dirt pipe |

1, when the fault can not be ruled out and the need to repair, please contact the vendor or authorized service station links, do not disassemble the machine repair.

2, the dehumidifier is running or stopped, will hear the sound of the refrigerant cycle, which is normal but not a malfunction.

3, hot air exhaust outlet is normal.

# Six, main technical parameters

| Number | Item | Unit | Parameters |
| --- | --- | --- | --- |
| 1 | Shape dimension (long x wide x high) | mm | 480×400×1080 |
| 2 | Total input power | kW | 2.0 |
| 3 | Refrigerants code |  | R22 |
| 4 | Rated voltage | V | 220 |

# Seven, accessories list

| Name | Quantity | Note |
| --- | --- | --- |
| Bottom round | two |  |
| water pipe | one |  |
| indicator light | one |  |
| Product specifications | one |  |

# Contact Us

Beijing Yiyuan Economic Trade Ltd

Tel: 8610-8869-1269

8610-5269-0547

Fax: 8610-6868-3582

8610-5269-0549

Tea web: http://www.teanet.com.cn

English Web: http://english.teanet.com.cn

Tea E-mail: sales@teanet.com.cn

Machine Web: http://www.mycotrade.com/enm.htm

Machine E-mail: sales@mycotrade.com

Agri web: http://www.seednet.com.cn

Agri Email: sales@seednet.com.cn

Tour web: http://www.ailitrip.com

Tour Email: aili@ailitrip.com